DeAuth attack

Start Airgeddon

cd ~/airgeddon

sudo bash airgeddon.sh

Run through setup process

Select network interface

Put interface into monitor mode

Select ‘Dos attacks menu’

Select ‘Explore for targets’ Wait until you see your target network and then use Ctrl + C to stop target identification

Select your target

Select ‘DeAuth/disassoc amok mdk4 attack’

Begin the attack, use Ctrl + C to stop

When attack is finished, put interface back into managed mode